## Slide 1
MXT 301: RADIOGRAPHIC TECHNIQUE II: LOWER LIMBS
BY
DR. M.P.OGOLODOM
THE RRBN RETRAINING COURSE FOR
X-RAY TECHNICIANS
IN PORT HARCOURT
23RD OCTOBER, 2026

## Slide 2
TOES
Indications
Fractures, dislocations, pain , swollen, pathologies, foreign bodies, RTA, trauma, assault
Patients’ Preparations
Proper identification
Explain the procedures to the patient
Reassure the patient
Remove materials around the fingers and hand
Projections
Dorsiplantar (anteroposterior)
Dorsiplantar (anteroposterior)Oblique
Lateral
Patient’s Positioning
Dorsiplantar (AP)
Patient seat on the X-ray couch with knees flexed
Place plantar aspect of the affected foot on film
Support the side under examination with knee of the other leg to immobilize foot
Place anatomical marker (R or L)

## Slide 3
Collimate beam properly
Apply protection
Cassette Size
13x18cm or 24x18cm split using lead rubber divider
Direction of Central Ray and Centring Point
DCR: Vertical 90 degree
CP: Head of THIRD metatarsal or the individual toe under examination.
Exposure Factors
mAs: 1.5-2.5
KvP: 50-55
Film Focal Distance(FFD): 100cm
Lateral Projection for Toes
Lie the patient on the X-ray couch on the affected side with the hip and knee flexed
Rest the unaffected leg in a comfortable position in front of or behind the affected leg.
Place the foot in the true lateral position with the knee raised on a pad and the film under the toes
Immobilize the foot

## Slide 4
Collimate beam properly
Apply protection
Cassette Size
13x18cm or 24x18cm split using lead rubber divider
Direction of Central Ray and Centring Point
DCR: Vertical 90 degree
CP: Head of FIRST metatarsal or the individual toe under examination.
Exposure Factors
mAs: 1.5-2.5
KvP: 50-55
Film Focal Distance(FFD): 100cm
Patient Positioning for Dorsiplantar (anteroposterior)Oblique
From the AP position, the affected limb is allowed to lean medially to bring the plantar surface of the foot approximately 45 degrees to the cassete
A 45 degree non-radiopaque pad placed under the side of the foot for support with opposite leg acting as a support.
Place anatomical marker (R or L)

## Slide 5
Collimate beam properly
Apply protection
Cassette Size
13x18cm or 24x18cm split using lead rubber divider
Direction of Central Ray and Centring Point
DCR: Vertical 90 degree
CP: Head of FIRST metatarsal or the individual toe under examination.
Exposure Factors
mAs: 1.5-2.5
KvP: 50-55
Film Focal Distance(FFD): 100cm
FOOT
Patient Positioning for Dorsiplantar (anteroposterior)
Patient seat on the X-ray couch with knees flexed
Place plantar aspect of the affected foot on film
Support the side under examination with knee of the other leg to immobilize foot
Place anatomical marker (R or L)

## Slide 6
Collimate beam properly
Apply protection
Cassette Size
24x18cm or 30x24cm split using lead rubber divider
Direction of Central Ray and Centring Point
DCR: Vertical 90 degree
CP: Dorsum of the foot to the Cubiod-navicular region
Exposure Factors
mAs: 2-4
KvP: 50-65
Film Focal Distance(FFD): 100cm
Patient Positioning for Dorsiplantar (anteroposterior)Oblique
From the AP position, the affected limb is allowed to lean medially to bring the plantar surface of the foot approximately 45 degrees to the cassete
A 45 degree non-radiopaque pad placed under the side of the foot for support with opposite leg acting as a support.
Place anatomical marker (R or L) .
DCR: Vertical
CP: Dorsum of the foot to the Cubiod-navicular region

## Slide 7
Lateral Projection for Foot
Seat the patient on the X-ray couch on the affected side with the hip and knee flexed
Rest the unaffected leg in a comfortable position in front of or behind the affected leg.
Place the foot in the true lateral position with the knee raised on a pad
Immobilize the foot
Collimate Beam and apply protection
Place anatomical marker (R or L)
DCR:: Vertical or Horizontal (if cassette is placed at the lateral part of the foot in case of pes planus[Flat foot])
CP: Cuboid-navicular area of foot.
ANKLE
Patient Positioning for Anteroposterior
Patient seat on the X-ray couch with legs extended and unaffected leg abducted.
Place the ankle on the film-cassette with the joint flexed 90 degrees
Rotate the ankle medially until both malleoli are equidistant from the couch top.
Immobilize the sole of the foot with a pad and sandbag
Place anatomical marker (R or L)
Collimate beam and apply protection
DCR: Vertical
CP: Midway between the malleoli
Cassette size : 12x10inch or 10x8inch

## Slide 8
Exposure factors:
Kvp: 55-70
mAs: 3-5
FFD/SID: 100cm
Lateral Projection for Ankle
Lie the patient on the X-ray couch on the affected side with the hip and knee flexed
Rest the unaffected leg in a comfortable position in front of or behind the affected leg.
Place the affected ankle in the true lateral position such as that both malleoli are superimposed with the knee raised on a pad
Immobilize the ankle
Collimate beam and apply protection
Place anatomical marker (R or L)
DCR:: Vertical
CP: Medial malleolus

## Slide 9
LEG(TIBIA-FIBULA)
Patient Positioning for Anteroposterior
Patient seat on the X-ray couch with legs extended and unaffected leg abducted.
Place the lower leg on the film-cassette with the ankle joint flexed 90 degrees with foot upright.
Include both ankle and knee joints on the film if possible.
Immobilize the sole of the leg with a pad and sandbag
Place anatomical marker (R or L)
Collimate beam and apply protection
DCR: Vertical
CP: Anterior aspect of the middle of lower leg midway between the ankle and knee joints
Cassette size : 12x10inch or 10x8inch
Lateral projection for Leg
Seat the patient on the X-ray couch on the affected side with the hip and knee flexed
Rest the unaffected leg in a comfortable position in front of or behind the affected leg.
Place the leg in the true lateral position with the knee raised on a pad
Immobilize the leg.
Collimate beam and apply protection
Place anatomical marker (R or L)
DCR:: Vertical or Horizontal (if cassette is placed at the lateral part of the leg in case of)
CP: Medial aspect of the middle of the lower leg midway between the ankle and knee joints.

## Slide 10
Exposure factors:
Kvp: 55-70
mAs: 5-8
FFD/SID: 100cm
NOTE: No use of grid
KNEE
AP Projection for Knee
Lie the patient on the X-ray couch on the affected side with legs extended and unaffected leg abducted
Place the affected knee on the film and flex the joint slightly
Ensure that the patella is central over the femur
Immobilize the leg
Collimate beam and apply protection
Place anatomical marker (R or L)
Cassette size : 12x10inch or 10x8inch
DCR:: Vertical
CP: 2.5cm below the apex of the patella
Exposure factors
Kvp: 55-75, mAs: 5-10 and FFD: 100cm

## Slide 11
Lateral projection for Knee
Lie the patient on the X-ray couch on the affected side with the knee flexed at 45 or 90 degrees
Rest the unaffected leg in a comfortable position in front of the affected leg.
Place the knee in the true lateral position
Immobilize the leg and ankle with sandbag.
Collimate beam and apply protection
Place anatomical marker (R or L)
DCR:: Vertical or Horizontal (if cassette is placed at the lateral part of the leg in case of)
CP: Middle of the superior border of the medial tibia condyle
PA for Patella
Patient lie prone on the table with knee slightly flexed
Foam pads are placed under the ankle and thigh for support
The limb is rotated to centralize the patella
The centre of the cassette is the level of the crease of the knee
Immobile the leg
Place anatomical marker
Collimate
DCR: Vertical
CP: In the midline to the skin crease behind the knee