## Slide 1
MXT 209: RADIOGRAPHIC TECHNIQUE 1:UPPER LIMBS
BY
DR. M.P.OGOLODOM
THE RRBN RETRAINING COURSE FOR
X-RAY TECHNICIANS
IN PORT HARCOURT
23RD OCTOBER, 2026

## Slide 2
FINGERS
Indications
Fractures, dislocations, pain , swollen, pathologies, foreign bodies, RTA, trauma, assault
Patients’ Preparations
Proper identification
Explain the procedures to the patient
Reassure the patient
Remove materials around the fingers and hand
Projections
Dorsipalmar (posteroanterior)
Lateral
Patient’s Positioning
Dorsipalmar(PA)
Patient seat alongside the X-ray couch
Place palmar aspect of the fingers under examination on film
Separate fingers slightly
Immobilize hand and wrist joint with sandbag
Place anatomical marker (R or L)

## Slide 3
Collimate beam properly
Apply protection
Cassette Size
13x18cm or 24x18cm split using lead rubber divider
Direction of Central Ray and Centring Point
DCR: Vertical 90 degree
CP: At the level of the proximal interphalangeal joint of the fingers or finger under examination.
Exposure Factors
mAs: 1.5-2.5
KvP: 50-55
Film Focal Distance(FFD): 100cm
Lateral Projection for Ring and Little fingers
From the PA position, the medial border of the hand is place on the film
Extend and separate ring and little fingers
Support ring finger with foam pad
Flex other fingers

## Slide 4
Immobilize the hand and wrist with sandbag
Place anatomical marker
Collimate beam properly
Apply protection
Cassette Size
13x18cm or 24x18cm split using lead rubber divider
Direction of Central Ray and Centring Point
DCR: Vertical 90 degree
CP: Proximal interphalangeal joint of the fingers or finger under examination.
Exposure Factors
mAs: 1.5-2.5
KvP: 50-55
Film Focal Distance(FFD): 120cm
NOTE: The image should include the tip of the finger and distal 3rd of the metacarpal

## Slide 5
THUMB
Projections
PA or AP and Lateral
Patient’s Positioning for PA Thumb
Seat patient alongside the X-ray couch
Extend arm, wrist and forearm
Place medial border of the hand on the film
Rotate hand medially until palmar aspect is 15 degree to film
Extend thumb and rest on a small radiolucnt pad
Avoid exerting pressure on thenar eminence
Immobilze hand with sandbag
Place anatomical marker
Collimate beam properly
Direction of Central Ray and Centring Point
DCR: Vertical
CP: Metacarpophalangeal joint of the thumb
NOTE: Increase the FFD to compensate for the large OFD

## Slide 6
Mediolateral Projection of Thumb
From the PA position, the palm of the hand is raised slightly with the fingers partially flexed and supported on foam pad.
The lateral aspect of the thumb is in contact with the cassette
Direction of Central Ray and Centring Point
DCR: Vertical
CP: Head of FIRST metacarpophalangeal joint
HAND
Projections
Dorsipalmar(PA)
Dorsipalmar(PA) Oblique
Lateral
Patients’ Positioning for PA
Patient is seated alongside the X-ray couch with arm nearest to the table
The forearm is pronated and placed on the table with palmer surface of the hand in contact with the cassette
The fingers are separated and extended but relaxed to ensure that they remain in contact with the cassette
The wrist is adjusted so that the ulnar and radius styloid processes are equidistant from the cassette
Immobilize hand with sandbag over the lower forearm

## Slide 7
Place anatomical marker
Collimate Beam and apply protection
Cassette Size
24x30cm(12x10inch) or 24x18cm (10x8 inch)
DCR: Vertical
CP: Over the head of the THIRD metacarpal
Exposure factors
mAS: 2-4
KvP:50-55
FFD:100cm
Patients’ Positioning for PA Oblique
From the PA position, the hand is externally rotated 45 degrees with fingers extended
The fingers should be separated slightly and hand supported on 45 degree foam pad
Immobilize hand with a sandbag placed over the lower end of the forearm
Place anatomical marker (R or L) and collimate beam to area of interest.
DCR: Vertical
CP: Head of the FIFTH metacarpal
NOTE: This projection help to demonstrates joint spaces clearly.

## Slide 8
Patients’ Positioning for Lateral Hand
From the PA position, the hand is externally rotated 90 degrees
The palm of the hand is perpendicular to the cassette with the fingers extended and thumb abducted and supported parallel to the film on radio-opaqe pad
The radial and ulnar styloid processes are superimposed
DCR: Vertical
CP: Over the head of the SECOND metacarpal
Note: This projection is commonly done to identify the foreign bodies.
Patients’ Positioning for Anteroposterior (AP) both Hands(Ball Catcher)
The patient may seat facing the table
Both forearms are supinated and placed on the table with the dorsal surface of the hands in contact with the cassette
From this position, both hands are rotated medially 45 degree into a Ball-catching position
The fingers and thumb are separated
Immobilized the lower forearms with sandbag
Place anatomical marker and collimate beam, and apply protection
DCR: Vertical
CP: A point midway between the hands at the level of the FIFTH metacarpophalangeal joint.

## Slide 9
WRIST
Projections
Posteroanterior (PA)
Lateral
PA Ulnar deviation for Scaphod
Superoinferior(axial) projection for carpal tunnel
Patient’s Positioning for PA
Seat patient alongside the X-ray couch
Rest palm, wrist and lower forearm in a straight line on film
Place small pad under metacarpophalangeal joints of hand to maintain wrist in close contact with film
Immobilize the wrist and forearm
Place anatomical marker(R or L)
Collimate beam and apply protection
DCR: Vertical
CP: Midway between the ulnar and radial styloid processes
Cassette Size
24x30cm or 24x18cm
Exposure factors
Kvp: 50-60, mAs:3-5 and FFD: 100cm

## Slide 10
Patient’s Positioning for Lateral Wrist Joint
Seat patient alongside the X-ray couch
Extend hand, wrist and forearm in a straight line on film
Rotate the forearm into the lateral position and rest the 5th finger and medial aspect of the hand and lower forearm in a straight line on film
Ensure ulnar and radial styloid processes are superimposed
Immobilize the forearm
Place anatomical marker(R or L)
Collimate beam and apply protection
DCR: Vertical
CP: Radial styloid processes
Cassette Size
24x30cm or 24x18cm
Exposure factors
Kvp: 55-65, mAs:3-5 and FFD: 100cm

## Slide 11
Patient’s Positioning for PA Ulnar deviation for Scaphoid
Seat patient alongside the X-ray couch
Rest palm, wrist and lower forearm on the film with ulnar deviation of hand
Ensure ulnar and radial styloid processes are equidistant
Immobilize the forearm
Place anatomical marker(R or L)
Collimate beam and apply protection
DCR: Vertical
CP: Midway between the ulnar and radial styloid processes
Cassette Size
24x30cm or 24x18cm
Exposure factors
Kvp: 50-60, mAs:3-5 and FFD: 100cm
NOTE: It is important to examine the patient again at least 14 days after the initial examination to properly demonstrates fracture scaphoid radiographically.

## Slide 12
Patient’s Positioning for Superoinferior (Axial) projection for carpal tunnel
Stand the patient with the back to the X-ray table and extend arm
Flex elbow and wrist, and with the fingers and thumb well separated press the hand palm down on to a film near the edge of the couch.
Ensure that the carpal region is in profile
Immobilize the hand with a foam pad if necessary
Place anatomical marker(R or L)
Collimate beam and apply protection
DCR: Vertical
CP: Midcarpal region
Cassette size: 24x18cm
FOREARM
Projections
Anteroposterior (AP)
Lateral
Patient’s Positioning for AP Forearm
Seat the patient alongside the X-ray couch with shoulder at the couch level.
Place forearm fully supinated with elbow extended
Include wrist and elbow if possible using long cassette size
Place anatomical marker(R or L)
Collimate beam and apply protection

## Slide 13
DCR: Vertical
CP: Anterior aspect of the middle of the forearm, midway between the wrist and elbow joints.
Cassette Size
43x35cm(17x14inch) or 35x35cm(14x14inch)
Exposure factors
Kvp: 50-60, mAs:3-5 and FFD: 100cm
Patient’s Positioning for Lateral Forearm
Seat the patient alongside the X-ray couch
Lower shoulder of affected side to same level as forearm.
Flex elbow at 90 degrees
Place medial border of forearm on film.
Include wrist and elbow if possible using long cassette size
Place anatomical marker(R or L)
Immobilize hand with sandbag
Collimate beam and apply protection
DCR: Vertical
CP: Lateral aspect of the forearm, midway between wrist and elbow joints
Cassette Size
43x35cm(17x14inch) or 35x35cm(14x14inch)
Exposure factors
Kvp: 55-65, mAs:3-5 and FFD: 100cm

## Slide 14
ELBOW JOINT
Projections
Anteroposterior (AP)
Lateral
Axial
Patient’s Positioning for AP Elbow Joint
Seat the patient alongside the X-ray couch with shoulder at the couch level.
Place forearm fully supinated with elbow extended on a film
Ensure that the patients’ thumb is touching the couch top if possible.
Place anatomical marker(R or L)
Immobilize the hand
Collimate beam and apply protection
DCR: Vertical
CP: In the midline 2.5cm distal to a line joining the lateral and medial epicondyles of the humerus
Cassette Size
24x18cm(10x8inch) or 30x24cm(12x10inch)
Exposure factors
Kvp: 55-65, mAs:3-5 and FFD: 100cm

## Slide 15
Patient’s Positioning for Lateral Elbow Joint
Seat the patient alongside the X-ray couch with shoulder, elbow and hand at the same level.
Flex elbow 90 degrees and rotate forearm into true lateral position with thumb uppermost.
Rest medial border of elbow on film
Place anatomical marker(R or L)
Immobilize the hand and wrist
Collimate beam and apply protection
DCR: Vertical
CP: Lateral epicondyle of the humerus
Cassette Size
24x18cm(10x8inch) or 30x24cm(12x10inch)
Exposure factors
Kvp: 55-65, mAs:3-5 and FFD: 100cm

## Slide 16
Patient’s Positioning for Axial Elbow Joint
Seat the patient alongside the X-ray couch with shoulder at the same level.
Flex elbow so that the hand is in contact with the shoulder
Rest elbow on film with upper arm at couch level
Place anatomical marker(R or L)
Immobilize the hand and wrist
Collimate beam and apply protection
DCR: Vertical or 30 degree towards the shoulder
CP: In the midline 5cm distal to the oleranon process
Cassette Size
24x18cm(10x8inch) or 30x24cm(12x10inch)
Exposure factors
Kvp: 55-65, mAs:3-5 and FFD: 100cm
NOTE: The choice of exposure factors depends on
Anatomical structure
Type of film material use
Energy of the beam

## Slide 17
ARM (HUMERUS)
Projections
Anteroposterior (AP)
Lateral
Inferiosuperior for surgical neck
Patient’s Positioning for AP Elbow Joint
Stand or sit the patient facing towards the X-ray tube.
Rotate the body slightly towards affected side
Place the arm in the anatomical position
Rest the hmerus against the film to include shoulder and elbow.
Place anatomical marker(R or L)
Collimate beam and apply protection
DCR: Horizontal or Vertical(If patient lying down supine)
CP: Anterior aspect of the humerus midway between the shoulder and elbow joints
Cassette Size
24x18cm(10x8inch) or 30x24cm(12x10inch), 43x35cm(17x14inch)
Exposure factors
Kvp: 55-70, mAs:10-12 and FFD: 100cm

## Slide 18
Patient’s Positioning for Lateral Arm
Stand or sit the patient facing towards the chest stand or upright cassette holder.
Slightly abduct and extend the arm and flex elbow
Rotate trunk away from the affected side until lateral aspect of the humerus rest on the film
Include shoulder and elbow.
Place anatomical marker(R or L)
Collimate beam and apply protection
DCR: Horizontal or Vertical(If patient lying down supine)
CP: Medial aspect of the humerus midway between the shoulder and elbow joints
Cassette Size
24x18cm(10x8inch) or 30x24cm(12x10inch), 43x35cm(17x14inch)
Exposure factors
Kvp: 55-70, mAs:10-12 and FFD: 100cm
Patient’s Positioning for Inferosuperior Projection of Arm
Patient lie supine on the couch and turn head away from the affected side.
Fully abduct arm if possible and support in a comfortable position
Vertically support cassette above the shoulder include upper humerus
Immobilize the arm
Place anatomical marker(R or L)
Collimate beam and apply protection
DCR: Horizontal or Vertical(If patient lying down supine)
CP: Head of humerus through the axial